## Slide 1
Development Of Automatic Flow Control System Based On LabView
Chemical Engineering Department
Du-Seob Kim
Seung-Gyu Ann
*Tae-Won Kang
Notes: 전반부 발표 : 안승규
후반부 발표 : 김두섭 지도교수 : 강태원

## Slide 2
CONTENTS
01.
Introduction
02.
03.
Simulation results
04.
Conclusion
Composition of equipment
Notes: 목차 : 서론  이론  장치의 구성  시뮬레이션 결과  결론

## Slide 3
01
Introduction

## Slide 4: 01. Introduction
4
Notes: 배경 : 산업의 발달/효과적인 제어의 필요성  부적절한 제어로 인한 사고사례  유량제어  자동제어//현재의 기술

## Slide 5: 01. Introduction
Flow control
To reach the desired value that fluid
through pipes or channel
Automatic control
To modify for desired value automatically
from data of process
5
Notes: 이론1 : 유량제어소개  자동제어소개

## Slide 6: 01. Introduction
John G. Ziegler
Nathaniel B. Nichols
Introduction of Ziegler-Nichols tuning method (1942)
Experimental method
6
Consistent oscillation
Divergence
Critical gain, KU
Critical oscillation period, PU
 | KC | τI | τD
P controller | 0.5KU | - | -
PI controller | KU/2.2 | 0.83PU | -
PID controller | KU/1.7 | 0.5PU | 0.125PU
Notes: 이론3 : Ziegler-Nichols 이론 : 비례 이득을 변화시키며 단위 계단 입력에 대한 시스템의 응답이 감쇠가 없는 임계 감쇠(Critical damping) 상태가 되는 임계이득(KU) 와 임계 진동 주기(PU)를 이용하여 P, I, D 계수 값을 선정하는 방법이 이용
각 제어기에 따른 계수는 표와 같이 계산됨

## Slide 7: 01. Introduction
LabView
Specialized program in measurement and control
Program based on graphic
Front panel
Control (Input)
Indicator (Output)
User interface
Block diagram
Source code similar
to flow chart
Non-sequential
programming
7
Notes: 이론4 : LabView  Front Panel and Block diagram

## Slide 8: 01. Introduction
8
Programming automatic flow system
based on LabView
Analysis and combination of relation
between software and hardware
Each variable setting of PID control
by Ziegler-Nichols tuning method
Development of optimized
automatic flow control system
Notes: 목적 : 랩뷰를 이용한 자동유량제어시스템 프로그래밍  소프트웨어와 하드웨어 사이의 관계 분석  Ziegler-Nichols 튜닝법을 통한 P, PI, PID 제어 각각의 변수를 설정  최적화된 자동유량제어시스템의 구축

## Slide 9
02
Composition of equipment

## Slide 10
02. Composition of equipment
Composition of software (Front panel)
10
Composition of software (Block diagram)

## Slide 11: 02. Composition of equipment
11

## Slide 12
02. Composition of equipment
TYPE-300
XE-151
MSD-2
Air filter regulator
Maximum supply pressure : 17 bar
Output range : 0-80 bar
Effect of supply pressure variation :Less them 0.01 bar
12

## Slide 13
02. Composition of equipment
TYPE-300
∙ Air filter regulator
∙ Maximum supply pressure : 17 bar
∙Output range : 0-8 bar
XE-151
∙ Pneumatic positioner
∙ Supply electric current range : 4- 20 mA
∙ Supply pressure range : 1.4~7 bar
MSD-2
∙ Multi spring diaphragm
∙ Air to open
∙ Spring range : 0.2-1.0 bar
∙ Max supply pressure : 1.4 bar
Air filter regulator
Maximum supply pressure : 17 bar
Output range : 0-80 bar
Effect of supply pressure variation :Less them 0.01 bar
13

## Slide 14
03
Simulation results

## Slide 15
03. Simulation results
KU= 5
KU= 6
KU= 7
KU= 8
1
SP = 1.2 m3/min
Setting the PID parameters using Ziegler-Nichols tuning method
15
 | KC | τI(min) | τD(min)
P controller | 3.5000 | - | -
PI controller | 3.1818 | 0.03091 | -
PID controller | 4.1176 | 0.01862 | 0.004655

## Slide 16
SP = 1.2 m3/min
KC = 3.5
Set point
 | KC | τI(min) | τD(min)
P controller | 3.5000 | - | -
PI controller | 3.1818 | 0.03091 | -
PID controller | 4.1176 | 0.01862 | 0.004655
03. Simulation results
Off set
P control using Ziegler-Nichols tuning method
16

## Slide 17
SP = 1.2 m3/min
KC = 3.2
τI = 0.03091 min
 | KC | τI (min) | τD(min)
P controller | 3.5000 | - | -
PI controller | 3.1818 | 0.03091 | -
PID controller | 4.1176 | 0.01862 | 0.004655
03. Simulation results
PI control using Ziegler-Nichols tuning method
17

## Slide 18
SP = 1.2 m3/min
KC = 4.12
τI = 0.01862 min
τD = 0.00466 min
 | KC | τI (min) | τD(min)
P controller | 3.5000 | - | -
PI controller | 3.1818 | 0.03091 | -
PID controller | 4.1176 | 0.01862 | 0.004655
03. Simulation results
PID control using Ziegler-Nichols tuning method
18

## Slide 19
SP = 1.2 m3/min
KC = 4.12
τI = 0.01862 min
τD = 0.00466 min
03. Simulation results
SP = 0.6 m3/min
SP = 0.9 m3/min
SP = 1.5 m3/min
Set point change
19

## Slide 20
03. Simulation results
33 % change
67 % change
Disturbance change
SP = 1.2 m3/min
KC = 4.12
τI = 0.01862 min
τD = 0.00466 min
20

## Slide 21
04
Conclusion

## Slide 22
P control | Confirmation of offset
PI control | Offset elimination
PID control | Offset elimination and faster response than PI control
Set point change | Stable response
Disturbance change | Stable response
04. Conclusion
22

## Slide 23
04. Conclusion
PID control by Ziegler-Nichols tuning method was successful
to control the flow rate
Software
Hardware
23

## Slide 24
Thank You!
Any Question?